## Slide 1: Design of a Class-A Common-Emitter RF Power Amplifier for the 433 MHz ISM Band
Ilias Ahmad
2006068
Mohammad Al Hosan
2006090
Shohan Ahmed Rifat
2006116
Md. Alamgir Islam
2006122
EEE 466 – Analog Integrated Circuits and Design Laboratory
Jan 2025 Level-4 Term-I Electronics G2
Final Project Presentation
Group- 04
Date : July 29,2025

## Slide 2: Outline
Abstract
Introduction
Design Analysis
Design Methods
Design: Simulation
Implementation: Demonstration
Novelty
Future Work
CO/PO
References
Presented by: 20060122

## Slide 3: 1. Abstract
Designed a Class-A common-emitter RF power amplifier targeting the 433 MHz ISM band.
Used inductor-integration to restrict AC power flow and an impedance matching network for stable operation.
Performed circuit simulation in Cadence to validate performance metrics.
Achieved Power Gain of 10.1138 dB and PAE of 7.52%, demonstrating effective design.
Presented by: 20060122

## Slide 4: 2 Introduction
ISM band (433 MHz) is popular for license-free, short-range communication.
RF Power Amplifiers are critical in wireless systems, used to boost signal strength.
Class-A amplifiers offer linearity but are less efficient, requiring optimized bias and matching.
Our project aligns with applications like wireless sensor nodes and RF transmitters.
Presented by: 20060122

## Slide 5
3.1 Design: Identification of Scope
Parameter | Value
Topology | Common-Emitter (CE)
Frequency | 433 MHz
Gain | ≥ 10 dB
Power-Added Efficiency (PAE) | ≥ 5%
Saturation Power (Psat) | ≥ 17 dBm
Technology | gpdk090 or tsmc18
Presented by: 20060122

## Slide 6: 3.2 Literature Review
İsa Kocakarin (Istanbul, 2011): In his B.Sc. thesis, Kocakarin explores RF amplifier design at 433 MHz using a Class-A Topology .The study emphasizes optimization of gain and stability, achieving over 30 dBm output with low noise and efficient power transfer.
NXP Semiconductors (2014): In their Application Note AN11504, NXP presents a detailed design for the BFU590Q transistor-based RF amplifier targeted at the 433 MHz ISM band. It covers key aspects such as gain optimization and impedance matching, critical for ISM applications.
Analog Devices (2003): The RF Power Amplifier Design Notes highlight design challenges in RF amplifiers, focusing on load-line theory, matching network design, and efficiency. These notes are essential for understanding amplifier architectures and the trade-offs between linearity and power efficiency.
Presented by: 20060122

## Slide 7: 3.3 Design: Problem Formulation (PO(b))
Design Requirement/Challenge | Details
Amplification Goals | Achieve minimum gain of 10 dB and Psat ≥ 17 dBm, with PAE ≥ 5% for efficient signal amplification.
Design Topology | Class-A Common-Emitter topology for linear amplification suitable for the ISM band.
Biasing and Stability | Inductor-based biasing for low noise and stability, ensuring reliable operation under varying conditions.
Impedance Matching | Ensure input/output matching to a 50Ω system with input return loss < -10 dB and output return loss < -20 dB.
Simulation and Validation | Use Cadence and QUCS Studio to simulate and validate performance metrics like gain, PAE, and impedance matching.
EEE 466 (2025) –Project Group 04
Presented by: 20060122

## Slide 8: 3.2 Design Methods (PO(a))
1. Circuit Selection
2. Simulation in Cadence ,Virtuoso
4. Extract S-parameters
(from Cadence Virtuoso)
5. Design Matching
Network in QUCS Studio
6. Simulate with Matching
Network in Cadence
7. Adjust and Finalize
Design in Cadence
Presented by: 20060068
3. Adjusting Q point

## Slide 9: Design: Simulation & Implementation: Demonstration
Presented by: 20060068

## Slide 10
EEE 466 (2025) –Project Group 04
Biasing Circuit(Adjusting Q point)
Biasing for,
Presented by: 20060068

## Slide 11
EEE 466 (2025) –Project Group 04
Biasing Circuit(Adjusting Q point)
Presented by: 20060068

## Slide 12
EEE 466 (2025) –Project Group 04
Biasing Circuit(Adjusting Q point)
Presented by: 20060068

## Slide 13: 3.3 Design: Circuit Diagram (Without Matching Network)
EEE 466 (2025) –Project Group 04
Presented by: 20060068

## Slide 14: S parameters (without matching network)
Presented by: 20060068

## Slide 15
EEE 466 (2025) –Project Group 04
Designing Matching Network(QUCS Studio):
Presented by: 20060068
Fig : QUCS Studio Matching Network Tools

## Slide 16
EEE 466 (2025) –Project Group 04
Designing Matching Network(QUCS Studio):
Presented by: 20060068
Fig : Matching Network Tools

## Slide 17
EEE 466 (2025) –Project Group 04
Class A Power Amplifier (Matching Network):
Presented by: 20060090

## Slide 18
EEE 466 (2025) –Project Group 04
S parameter (With Matching Network):
Presented by: 20060090

## Slide 19
EEE 466 (2025) –Project Group 04
:
Presented by: 20060090

## Slide 20
EEE 466 (2025) –Project Group 04
:
Presented by: 20060090

## Slide 21
EEE 466 (2025) –Project Group 04
Power Gain:
Presented by: 20060090

## Slide 22
EEE 466 (2025) –Project Group 04
Power Gain = 10.1138dB
Power Gain:
Presented by: 20060090

## Slide 23
Presented by: 20060090

## Slide 24
EEE 466 (2025) –Project Group 04
Voltage Harmonics():
Presented by: 20060090

## Slide 25
EEE 466 (2025) –Project Group 04
Power Harmonics():
Presented by: 20060090

## Slide 26
EEE 466 (2025) –Project Group 04
Simulation:
433MHz
Presented by: 20060090

## Slide 27
EEE 466 (2025) –Project Group 04
Presented by: 20060090

## Slide 28
Presented by: 20060090

## Slide 29
EEE 466 (2025) –Project Group 04
Simulation:
433MHz
Presented by: 20060090

## Slide 30
EEE 466 (2025) –Project Group 04
(Simulation):
Presented by: 20060090

## Slide 31
EEE 466 (2025) –Project Group 04
(Manual Calculation):
Presented by: 20060116

## Slide 32
EEE 466 (2025) –Project Group 04
Pin = 0.5*4.33m/2=1.0825mW Pout = 21.6678mW
Presented by: 20060116

## Slide 33
Input and Output Impedance:
Presented by: 20060116

## Slide 34
EEE 466 (2025) –Project Group 04
PAE (Manual Calculation):
+
-
Presented by: 20060116

## Slide 35
EEE 466 (2025) –Project Group 04
Presented by: 20060116

## Slide 36
EEE 466 (2025) –Project Group 04
Simulation:
+
-
Presented by: 20060116

## Slide 37
EEE 466 (2025) –Project Group 04
Presented by: 20060116

## Slide 38: 5.1 Novelty
Novelty Aspect | Details
Inductor- Integration | Improves stability and reduces noise, enhancing performance.
Optimization for 433 MHz ISM Band | Tailored for the specific challenges of the 433 MHz frequency range.
Impedance Matching Network | Custom matching network designed using S-parameters to enhance power transfer efficiency.
Simulation and Real-World Testing | Combines Cadence Virtuoso simulations with practical design validation.
Low-Power, High-Efficiency Design | Focus on optimizing PAE and thermal stability for IoT and sensor applications.
EEE 466 (2025) –Project Group 04
Presented by: 20060116

## Slide 39
5.2 comparison table of target and achieved specifications.
Parameter | Value (Required ) | Value (Achived )
Frequency | 433 MHz | 433MHz
Gain | ≥ 10 dB | 10.1138dB
Power-Added Efficiency (PAE) | ≥ 5% | 7.5%
Saturation Power (Psat) | ≥ 17 dBm | dBm
Technology | gpdk090 or tsmc18 | gpdk090
Parameter | Value (Required ) | Value (Achived )
Frequency | 433 MHz | 433MHz
Gain | ≥ 10 dB | 10.1138dB
Power-Added Efficiency (PAE) | ≥ 5% | 7.5%
Saturation Power (Psat) | ≥ 17 dBm | 
Technology | gpdk090 or tsmc18 | gpdk090
Presented by: 20060116

## Slide 40: 8. Future Work (PO(l))
Integration with Advanced Modulation Techniques
Optimization for Multi-Stage Amplifiers
Thermal and Power Efficiency Enhancement
Presented by: 20060116

## Slide 41: 6. Reflection on Individual and Team work
Phase | Duration | Activities | Responsible Members
Phase 1 | Week 8 | Literature Review, Background | Ilias(68), Rifat(116), Hosan(90), Alamgir(122)
Phase 2 | Week 9 | Circuit Design and Simulation in Cadence Virtuoso | Ilias, Rifat, Hosan
Phase 3 | Week 10 | S-parameters Extraction and Analysis, Matching Network Design in QUCS Studio | Hosan, Alomgir, Rifat
Phase 4 | Week 11 | Optimization and Tuning of Matching Network | Rifat, Alomgir, Ilias
Phase 5 | Week 12 | Testing and Validation of the Amplifier | Ilias, Rifat, Hosan
Phase 6 | Week 13 | Final Adjustments, Documentation, Presentation and Final Report Writing | Ilias, Rifat, Hosan, Alomgir
Presented by: 20060116

## Slide 42: 7 Communication to External Stakeholders (PO(j))
  Github Link
  YouTube Link
Presented by: 20060116

## Slide 43: 9. CO/PO Alignment
CO(s) | Key Contributions | Aligned PO(s)
CO1, CO2 | Application of semiconductor physics in analog circuit design and analysis of IC operation based on physics and control theory. | PO(a), PO(b)
CO3, CO4 | Designing solid-state integrated circuits and verifying performance using circuit simulation tools for complex device models. | PO(c), PO(e)
CO5, CO6 | Demonstrating effective teamwork and presenting designed analog devices/systems through interactive discussions and project presentations. | PO(i), PO(j)
CO7 | Applying skills in the design and presentation of Analog Integrated Devices/Systems, focusing on communication and design synthesis. | PO(j)
Presented by: 20060116

## Slide 44: 10. References
NXP Semiconductors, BFU590Q ISM 433 MHz PA Design Application Note (AN11504), NXP Semiconductors, 2014.
Analog Devices, RF Power Amplifier Design Notes, May 2003. [Online]. Available: https://www.analog.com/media/en/training-seminars/tutorials/MT-101.pdf
İ. Kocakarin, “RF Power Amplifier Design Operating at 433 MHz,” B.Sc. thesis, Dept. of Electrical and Electronics Eng., Yeditepe Univ., Istanbul, Turkey, 2016. [Online]. Available: https://www.academia.edu/42443047
I. J. Bahl, Fundamentals of RF and Microwave Transistor Amplifiers, Wiley, 2003.
Presented by: 20060116